Customer  Name_DIAMOND MATERIALS_____________    SN____2015___

Remote Setpoint RSP High Range 20 ma__BELT SCALE_400___ eng units_TPH_

Process Variable PV  High Range 20 ma_Dust-Flow Scale __50_ eng units_TPH__

Parameter Value Charts

Tuning

PWR Back ..Disabled

Prop Band.. 10%

Reset 1 ..20

Rate 1.. 1

Load Line 1 ..0%

RSO.. .3%

RSP Bias ..0

No of PID 1

Config

1 CONTROL TYPE  standard

2 LINE FREQ 60 hz

3 PV SOURCE  PV1

4 REMOTE SETPOINT  enabled

5 OUTPUT 2  Alm RLY on

6 OUTPUT 3 Alm RLY on

7 OUTPUT 4 Alm RLY on

8 ANALOG RANGE 1 4-20 ma

12 CONTACT 1 manual

13 CONTACT 2 remote sp

14 CONTACT 3 second sp

15 CONTACT 4  second pid

16 CONTACT 5  alarm ack

17 LOOP NAME FIBER

PV1 Input

1 PV1 TYPE 4-20 ma

3 DECIMAL 00.00

4 LINEARIZE none

5 LOW RANGE  0.00

6 HIGH RANGE 15.00

7 SP LOW LIM 0.00

8 SP HIGH LIM 15.00

9 sp Ramp off

10 FILTER  1

11 OFFSET 0.00

12  GAIN 1.00

13 RESTORE last mode

Control

1 ALGOrythem  pid

2 D SOURCE pv

3 ACTION 1 reverse

4 PV BREAK 0

5 LOW OUT 0

6 HIGH OUT 100

Alarms

1 ALARM TYPE 1 High ALARM

2 alarm sorce-1 1 PV1

3 alarm sp-1   1.800

4  deadband-1  .02

6  Alarm output 3

7 latching-1 no latch

8 ACK 1 enabled

8 PWR up1 normal

10 message-1  scale plugged

11 Alarm type 2 BAND

12  Alarm Setpoint 2  .1

13 dead band .02

16 Alarm out 2   2

17 Latch 2  no latch

18 ACK 2 disabled

19 PWR up 2 normal

20 message-2 Deviation

21 Fault Alarm 1

Remote Setpoint

1 type 1-5/4-20

2 rsp lo range  0.00

3 rsp Hi range 4.00

4 rsp lo  0.00

5 rsp hi  4.00

6 tracking  no

7 bias lo  -10.00

8  bias high  10.00

9  rsp fixed  remote SP

Self Tune

1 disabled

2

3

4

5

6

7

8

9 0.2

10 7200

11 0.1

Special

1 off

2

3 last out

4 manual

5 last out

6 last sp

7 1

Security

1 code 0

2 sp adjust  unlocked

3 auto man  unlocked

4 sp select   locked

5 alarm ack  unlocked

6 tuning  locked

7 configure  locked