BURNER ANALYSIS SHEET			Date:

Company:

Plant:

Probe Placement:     Dryer    Dryer Exit Duct    Stack

Fuel:        	                               Aggregate Moisture:      %  	Mix Temp:     °F  	Product:

Oil Viscosity Target:       SSU		Draft Target:    ″ WC

| TIMe (HH:MM) | tph | BurnER posIT. 0-10 | ExhAUST DampER PosIT. 0-10 | dryer draft 0-1” | DRYER exit temp | BAGHOUSE PRESSURE DROP 0-10” | COMP AIR PRESS | Fuel ValvE POSIT. 0-10 | BlowER Damp POSIT. 0-10 | fuel presS. | OIL TEMP °f | oXYGEN % | CARBON MONOXIDE PPM | CORRECTIVE ADJUSTMENT affecting next row of readings |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

BURNER ANALYSIS SHEET				Date: 12/29/2009

Company: Clarence Richard Company

Plant: Minnetonka

Probe Placement:     Dryer    Dryer Exit Duct    Stack

Fuel: #6 Oil  	                               Aggregate Moisture: 5.1 %  	Mix Temp: 300 °F  	Product: Base

Oil Viscosity Target: 92 SSU 		Draft Target: 0.3″ WC

| TIME HH:MM | tph | BurnER posIT. 0-10 | ExhAUST DampER PosIT. 0-10 | dryer draft 0-1” | DRYER exit temp | BAGHOUSE PRESSURE DROP 0-10” | COMP AIR PRESS | Fuel ValvE POSIT. 0-10 | BlowER Damp POSIT. 0-10 | fuel presS. | OIL TEMP °F | oXYGEN % | CARBON MONOXIDE PPM | CORRECTIVE ADJUSTMENT affecting next row of readings |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 07:00 | 250 | 4 | 4.0 | 0.50 | 225 | 4.9 | 104 | 4.1 | 4.8 | 150.0 | 125 | 16.0 | 1500 | Reduce fuel pressure |
| 07:30 | 250 | 4 | 4.0 | 0.45 | 235 | 4.4 | 104 | 4.1 | 4.8 | 140.0 | 125 | 15.5 | 1200 | Reduce fuel pressure |
| 07:40 | 250 | 4 | 4.0 | 0.55 | 195 | 4.9 | 104 | 4.1 | 4.8 | 130.0 | 125 | 14.0 | 600 | Increase fuel pressure |
| 07:50 | 250 | 4 | 4.0 | 0.45 | 235 | 4.4 | 104 | 4.1 | 4.8 | 140.0 | 125 | 15.5 | 1200 | Increase fuel temp |
| 08:00 | 250 | 4 | 4.0 | 0.40 | 240 | 4.4 | 104 | 4.1 | 4.8 | 140.0 | 140 | 13.0 | 400 | Close exhaust damper |
| 08:10 | 250 | 4 | 3.0 | 0.30 | 250 | 4.0 | 104 | 4.1 | 4.8 | 140.0 | 140 | 11.0 | 375 | Close exhaust damper |
| 08:20 | 250 | 4 | 2.5 | 0.25 | 250 | 3.8 | 104 | 4.1 | 4.8 | 140.0 | 140 | 9.0 | 375 | Open exhaust damper |
| 08:30 | 250 | 4 | 3.0 | 0.30 | 250 | 4.0 | 104 | 4.1 | 4.8 | 140.0 | 140 | 11.0 | 375 | Decrease compressor air press. |
| 08:40 | 250 | 4 | 4.0 | 0.28 | 245 | 3.9 | 94 | 4.1 | 4.8 | 140.0 | 140 | 10.8 | 475 | Increase compressor air press. |
| 08:50 | 250 | 4 | 4.0 | 0.33 | 255 | 4.1 | 115 | 4.1 | 4.8 | 140.0 | 140 | 11.2 | 275 | Document target visc., draft |