** Written Energy Control Procedure for Equipment Lockout Tagout**

** Written Procedure for working in Confined Space**

# Company: Land Paving

# Location:

# Date:

# Equipment:  Pugmill

# Task: inspection tips..

# Project Manager:

Emergency Response Instructions:

Emergency Response Telephone Numbers:

Fire Department:               Ambulance:               Supervisor:

# Select all that apply

| X | Procedure Category | Suggested Equipment/Permits/Training |  |  |
| --- | --- | --- | --- | --- |
|  | Safety Tools | Scaffolding |  |  |
|  |  | Coveralls | 1 | 5 |
|  |  | Eye Protection |  |  |
|  |  | Fall Protection |  |  |
|  |  | Traffic Barriers |  |  |
|  |  | Radio |  |  |
|  |  | Vent Fan |  |  |
|  |  | Air Quality Monitor |  |  |
|  |  | ARC Flash PPE |  |  |
|  |  | ladder |  |  |
|  | Permitted Confined Space | Permit |  |  |
|  |  | Buddy System |  |  |
|  |  | Air Quality Monitor |  |  |
|  |  | High Temperature Stress |  |  |
|  |  | Venting or Exhaust Fan locked on |  |  |
|  |  | Oxygen Depletion, Welding |  |  |
|  | ARC Flash Prevent & Protect | ARC Flash training up to date and verified |  |  |
|  |  | Verify correct ARC Flash PPE available |  |  |
|  |  | Electrical LOTO verified |  |  |

| X | Lockout Category | Suggested Lockouts Specify Order | Lock | Un-Lock |
| --- | --- | --- | --- | --- |
|  | Electrical 1 | Mixer Motor Circuit Breaker | 5 | 3 |
|  | 2 | Asphalt Pump Motor Circuit Breaker | 5 | 3 |
|  | 3 | RAP Feed Conveyor Motor Circuit Breaker | 5 | 3 |
|  | 4 | Slide Out Chute Motor Circuit Breaker | 5 | 3 |
|  | 5 | Slat Motor Circuit Breaker |  |  |
|  | 6 | Hot Oil Circulating Pump Motor Circuit Breaker |  |  |
|  | 7 | Locking hasp on Motor Control Panel doors |  |  |
|  | 8 | Lockout main circuit breaker |  |  |
|  | 9 | Lock Control Room |  |  |
|  | 10 |  |  |  |
|  | 11 |  |  |  |
|  | 12 |  |  |  |
|  | 13 |  |  |  |
|  | 14 |  |  |  |
|  | 15 |  |  |  |
|  | 16 |  |  |  |
|  | Gravity 1 | Empty Feed Bins and weigh Hoppers |  |  |
|  | 2 |  |  |  |
|  | 3 |  |  |  |
|  | Pneumatic 1 | Disconnect All Pressure Lines from Cylinders |  |  |
|  | 2 | bleed and shut off valve to tower | 4 | 2 |
|  | Mechanical 1 | Restrain Gate with Chain or Bolting Bar |  |  |
|  | 2 | Restrain Mixer Shaft from Rotation(when replacing tips) |  |  |
|  | 3 | Barricade Truck Traffic |  |  |
|  | Hydraulic 1 | Disconnect All Pressure Lines from Cylinders |  |  |
|  | 2 |  |  |  |
|  | Thermal 1 | Lockout Hot Oil Circulation |  |  |
|  | 2 | Lockout Manual Fuel Valve (Gas), Bleed Gas Lines |  |  |

Procedure Explanation and Additional Comments:

|  | open top door. | 1 | 4 |
| --- | --- | --- | --- |
|  | chaining slide out in place | 3 | 4 |
|  | empty bins, weigh hoppers | 2 |  |
|  | chain pug mill door.. | 3 | 4 |
|  | inspected | 6 | 1 |