CUSTOMER NAME CRC/Border States    S/N 2031   DATE /7/09/2009

Remote Setpoint (RSP) High Range (20 ma):       	ENG Units:

Process Variable (PV1) High Range (20 ma):       	ENG Units:

PARAMETER VALUES

TUNING

1 POWER BACK		DISABLED

2 PROP BND:1		10%

3 RESET:1			20

4 RATE:1			1

5 LOAD LINE:1		0%

6 RSP RATIO			0.3%

7 RSP BIAS			0

8 NO. OF PID			1

CONFIG

1 CONTROL TYPE 		STANDARD

2 LINE FREQ			60HZ

3 PV SOURCE 		PV1

4 REMOTE SETPOINT	ENABLED

5 OUTPUT 2 			ALM RLY ON

6 OUTPUT 3			ALM RLY ON

7 OUTPUT 4			ALM RLY ON

8 ANALOG RANGE 1	4-20mA

9 ANALOG RANGE	2

10 ANALOG RANGE 3

11 ANALOG RANGE 4

12 CONTACT 1		MANUAL

13 CONTACT 2		DOWN KEY

14 CONTACT 3		FAST

15 CONTACT 4		SECOND PID

16 CONTACT 5		ALARM ACK

17 LOOP NAME		FIBER

PV1 INPUT

1 PV1 TYPE 			4-20mA

2 DEGREES

3 DECIMAL			XX.XX

4 LINEARIZE			NONE

5 LOW RANGE		0.00

6 HIGH RANGE		15.00

7 SP LO LIM			0.00

8 SP HI LIM			15.00

9 SP RAMP			OFF

10 FILTER			1

11 OFFSET			0.00

12 GAIN			1.00

13 RESTORE			LAST MODE

CONTROL

1 ALGORITHM		PID

2 D SOURCE			PV

3 ACTION:1			REVERSE

4 PV BREAK			0

5 LOW OUT			0

6 HIGH OUT			100

ALARMS

1 ALARM TYPE:1		HIGH ALARM

2 ALARM SOURCE:1	PV1

3 ALARM SETPOINT:1	1.800

4 DEADBAND:1		0.02

5

6 ALARM:1 OUTPUT	3

7 LATCHING:1		NO LATCH

8 ACK:1			ENABLED

9 POWER UP:1		NORMAL

10 MESSAGE:1		SCALE PLUGGED

11 ALARM TYPE:2		BAND

12 ALARM SETPOINT:2	0.1

13 DEADBAND:2		0.02

14

15

16 ALARM:2 OUTPUT	2

17 LATCHING:2		NO LATCH

18 ACK:2			DISABLED

19 POWER UP:2		NORMAL

20 MESSAGE:2		DEVIATION

21 FAULT			ALARM 1

REMOTE SETPOINT

1 TYPE V/mA		1-5/4-20

2 RSP LO RANGE		0.00

3 RSP HI RANGE		4.00

4 RSP LOW			0.00

5 RSP HIGH			4.00

6 TRACKING			NO

7 BIAS LOW			-10.00

8 BIAS HIGH			10.00

9 RSP FIXED			REMOTE SP

SELF TUNE

1 TYPE			DISABLED

2 PRETUNE

3 TUNE PT

4 OUT STEP

5 LOW LIMIT

6 HI LIMIT

7 TIMEOUT

8 MODE

9 NOISE BAND		0.2

10 RESPONSE TIME		7200

11 DEAD TIME		0.1

SPECIAL

1 AUTO TRIP			OFF

2 TRIP DEVIATION

3 DES OUTPUT		LAST OUT

4 POWER UP			MANUAL

5 POWER UP:OUT		LAST OUT

6 POWER UP:SP		LAST SP

7 NUMBER OF SP		1

SECURITY

1 SECURITY CODE		0

2 SP ADJUST			UNLOCKED

3 AUTO/MANUAL		UNLOCKED

4 SP SELECT			LOCKED

5 ALARM ACK		UNLOCKED

6 TUNING			LOCKED

7 CONFIGURE		LOCKED